## Slide 1
STATE FORECASTING LAYER
Karnataka does not need another model demo. It needs confidence before schedule lock-in.
GridSense AI turns solar and wind variability into plant-level and cluster-level forecasts with uncertainty, physics checks, and operator-readable reasons.
24-hour operating view
Forecast line + confidence band + drivers + clamp reason
20.4%
BETTER THAN PERSISTENCE
33.9 MW vs 42.6 MW RMSE
5
KARNATAKA ASSETS
3 solar plants + 2 wind clusters
1-48h
FORECAST HORIZON
day-ahead and intra-day updates
0
SCADA MODIFICATIONS
forecasting layer; CSV and API out
GridSense AI | Theme 10 KREDL / KSPDCL | repo-derived deck
01

## Slide 2
WHY IT MATTERS
Every cloudy hour and wind ramp becomes a rupee-and-reliability decision.
01
Weather shifts
Cloud cover, GHI, wind speed and direction move faster than static schedules.
02
Forecast error
Operators over-schedule, under-schedule, or rely too much on backup power.
03
Grid imbalance
Confidence is missing exactly when renewable penetration is rising.
04
Penalty exposure
DSM deviations and curtailment risk become real taxpayer money.
The pitch is not "our AI is clever." The pitch is: schedule with quantified confidence, explain why the number moved, and keep existing SLDC systems intact.
Source: Theme 10 prompt, SUBMISSION.md, WIN_AUDIT.md
02

## Slide 3
ADOPTION PATH
GridSense is a layer, so government can pilot it without touching SCADA.
Existing SCADA
Hourly generation export from plant historian
GridSense API
FastAPI /forecast, /forecast/cluster, /forecast/bulk
Forecast layer
Baseline + residual + physics + uncertainty + explanations
Operator outputs
Dashboard, JSON, Excel-ready CSV, compliance report
No replacement
SLDC keeps current dashboards and workflows.
Masked data ready
Synthetic SCADA is physics-based and reproducible.
Air-gap logic
Explanations are deterministic; no hosted LLM on sensitive data.
Source: README.md, SUBMISSION.md, src/api/main.py
03

## Slide 4
WHAT IS UNIQUE
The build is a fusion pipeline, not a single fragile model.
1. Baseline
Chronos-Bolt zero-shot time-series forecast from 168h context
2. Residual
Open-Meteo weather adjusts sudden cloud and wind changes
3. Physics
Clear-sky GHI caps, turbine curves, rated limits, non-negative output
4. Explain
Offline deterministic reasons, confidence bands, Kannada-ready templates
Why this matters: a forecast that is numerically plausible but physically impossible will not survive a control room. GridSense corrects before the number reaches the operator.
Source: src/pipeline/orchestrator.py, baseline_forecaster.py, residual_adjuster.py, physics_constraints.py
04

## Slide 5
MEASURED PROOF
The prototype already beats yesterday-as-tomorrow scheduling.
Persistence baseline
42.6 MW
GridSense AI
33.9 MW
20.4%
RMSE improvement vs persistence
Why the metric matters
Persistence is the simple operator baseline: tomorrow looks like yesterday. Beating it is the first honest hurdle before any AI claim deserves trust.
Metric source: models/baseline/metrics.pkl. Current values: RMSE 33.901 MW, persistence RMSE 42.615 MW.
Source: models/baseline/metrics.pkl
05

## Slide 6
OPERATOR TRUST
Operators get a decision, a range, and a reason - not model mysticism.
SOL_PAVAGADA_100 | 13:00 IST
66.5
MW
expected generation
58.2
75.1
confidence band
Reason: downward adjustment due to cloud cover; capped when clear-sky GHI makes higher output impossible.
cloud_fraction
0.37
residual_MW
-18.5
was_clamped
true
Offline templates are a deliberate product choice: exact MW values, deterministic wording, zero external LLM calls, and Kannada support in the test harness.
Source: README.md, src/pipeline/explainability.py, tests/test_harness.py
06

## Slide 7
GOVERNMENT FEASIBILITY
The non-negotiables are product constraints, not appendix claims.
Requirement
How GridSense satisfies it
Status
No system replacement
Reads exported CSV/JSON; returns REST and CSV outputs
Built
Masked data
Physics-based synthetic SCADA plus real weather inputs
Built
Explicit uncertainty
confidence_lower and confidence_upper in every response
Built
Explainable operations
Deterministic reason strings with drivers and clamp reasons
Built
No hosted LLM
No external AI API for sensitive data; offline explanation engine
Built
Deployment
FastAPI, Streamlit, Docker, CPU-first run path
Built
Source: SUBMISSION.md, Dockerfile, docker-compose.yml, src/api/main.py
07

## Slide 8
DEMO QUALITY
The demo proves an operating workflow, not just a pretty forecast chart.
Plant forecast
/forecast
Cluster view
/forecast/cluster
Bulk schedule
/forecast/bulk
Operator override
Maintenance, curtailment, outage knowledge enters the forecast.
Data quality
Gaps, flatlines, impossible values, spikes checked before forecast.
CERC compliance
Daily benchmark against regulatory thresholds.
Scheduler
06:00 day-ahead and 12:00 intra-day CSV reports.
Judges can see the same system three ways: dashboard for humans, API for integration, CSV for government operations.
Source: src/api/main.py, dashboard/app.py, src/scheduler.py, src/pipeline/data_quality.py
08

## Slide 9
SCALE AND IMPACT
A five-asset pilot can become Karnataka's renewable forecasting fabric.
NOW
5 assets
Pavagada, Koppal, Raichur, Chitradurga, Hassan
PILOT
1 region
Daily forecasts, operator overrides, compliance review
SCALE
50+ assets
Flexible regional clusters and scheduler outputs
STATE LAYER
100s MW decisions
Forecast confidence embedded before dispatch
Third-order effect: better forecasts mean fewer blind backup decisions, less avoidable curtailment, cleaner audits, and faster onboarding for the next renewable plant.
Source: README.md, EXPLANATIONS_AND_ROADMAP.md, SUBMISSION.md
09

## Slide 10
THE ASK
Pilot the layer where scheduling error already costs attention, money, and trust.
20%
Problem depth
Karnataka assets, CERC context, non-negotiables mapped
25%
Technical build
4-pass fusion, uncertainty, physics, tested APIs
25%
Deployability
No SCADA changes, Docker, CPU, CSV/API outputs
15%
Demo quality
Dashboard + API + bulk + compliance + override
15%
Long-term impact
Pilot-to-state roadmap with sovereign data path
90-day pilot
5 plants -> one region -> scheduled CSV + API integration proof
Team / contact / repo
[add team name] | [add GitHub URL] | docker-compose up --build
Source: evaluation criteria supplied by user, repo evidence
10